AGK REVISION WORKSHEET 1

NAME ……………………….. COURSE …………………..

MARKING GUIDE

- The principle of operation of firewire is;

- Positive coefficient of impedance, negative coefficient of inductance

- Positive coefficient of resistance, negative coefficient of capacitance

- Positive coefficient of inductance, negative coefficient of impedance

- Positive coefficient of capacitance, negative coefficient of resistance

- What type of extinguisher should be used on a fuel fire?

- Foam

- Water

- Dry powder

- Sand

- On what principle do smoke detectors work?

- Resistance and capacitance

- Ionisation and impedance

- Optical and ionisation

- Inductance and light diffraction

- An ion detector detects;

- Smoke and fire

- Smoke

- Overheat

- Light

- If an artificial feel unit is fitted it would be connected;

- In parallel with the primary controls

- In series with the primary controls

- In series with the secondary controls

- In parallel with the secondary controls

- In a twin jet fuel system what is the function of the feeder box?

- Equally distribute the fuel to each tank during refuelling

- Prevent pump cavitation

- Feed fuel to the volumetric top-off unit

- Control the amount of fuel remaining during fuel jettison

- A modern passenger airliner would normally be refuelled by which of the following methods?

- Over wing refuelling

- Suction refuelling

- Open line refuelling

- Pressure refuelling

- During fuel jettison, the aircraft is protected against running out of fuel by;

- High level float switches

- The crew remaining alert

- Preset jettison quantity switches

- Low level float switches

- To indicate that a refuelling bowser carries JET A1 aviation kerosene;

- Yellow and black stripes are painted on the refuelling hose

- JET A1 is printed in white letters on a black background positioned prominently on the vehicle

- JET A1 would be painted in 30cm high symbols on the side of the container

- The driver wears a yellow water and fuel proof jacket

- Fuel tank booster pumps are;

- Spur gear pumps – high pressure

- Centrifugal pumps – high pressure

- Spur gear pumps – low pressure

- Centrifugal pumps – low pressure

- The advantage of a float type fuel gauging system is;

- Simple

- Compensates for variations of SG

- Reads fuel quantity by mass

- Compensates for changes in aircraft attitude

- 3 & 4

- 2 & 3

- 1 only

- 1 & 3

- What are the sources of air available for engine start?

- APU, Ground Power Unit, cross bleed from another engine

- APU, cross bleed from another engine, bottles of compressed air

- Ground Power Unit, bottles of compressed air, LP compressor

- Cross bleed from another engine, bottles of compressed gas, Ground Power Unit

- The function of baffles in a fuel tank is;

- To prevent movement of fuel to the wingtip

- To prevent fuel surge during manoeuvring

- To prevent pump cavitation

- To reduce fuel flow at altitude

- The function of the fuel tank vent system is;

- To allow air pressure above the fuel to equalise with ambient

- To partially pressurise the tanks in flight

- To prevent pump cavitation

- To prevent movement of fuel to the wingtip

- 1, 2 & 3

- 2, 3 & 4

- 2 & 3

- 1 & 2

- A magneto is switched off by;

- Open circuiting the primary circuit

- Grounding the secondary circuit

- Open circuiting the secondary circuit

- Grounding the primary circuit

- An impulse coupling in a magneto is provided to;

- Generate high voltage and advance the spark for starting

- Increase the energy to the spark plug as RPM increases

- Generate high voltage and retard the spark for starting

- Allow a low energy value when ‘continuous ignition’ is selected

- A turbo-supercharger impeller is driven by;

- A connection through a gearbox connected to the crankshaft

- Diversion of exhaust gases by the waste gate using energy that would otherwise be wasted

- Excess torque from the reduction gearbox

- A ram air turbine

- A cylinder head temperature gauge measures;

- The temperature of the hottest cylinder

- The temperatures of all the cylinders and gives an average reading

- The temperature of the coolest cylinder

- The temperature of the two cylinders furthest away from each other and divided by two

- EPR is measures by the ratio of;

- Turbine pressure to combustion chamber inlet pressure

- High pressure compressor inlet pressure to exhaust pressure

- Low pressure compressor inlet pressure to high pressure compressor outlet pressure

- Exhaust pressure to low pressure compressor inlet pressure

- Where is EGT measured?

- In the jet pipe

- HP turbine outlet

- HP compressor outlet

- Combustion chamber

- How are the loads on an aircraft busbar connected?

- In series so that current reduces through the busbar as loads are switched off

- In parallel so that voltage reduces through the busbar as loads are switched off

- In parallel so that current reduces through the busbar as loads are switched off

- In series so that voltage reduces through the busbar reduces as loads are switched off

- In a modern airliner what hydraulic fluid is used?

- Synthetic

- Mineral

- Mineral/Alcohol

- Vegetable

- In a bootstrap air conditioning system what is the flow of the air?

- Goes through the primary heat exchanger, turbine and compressor

- Goes through the compressor, turbine and secondary heat exchanger

- Goes through the turbine, compressor and secondary heat exchanger

- Goes through the primary heat exchanger and the compressor

- The minimum height for door sills before a means of assisted escape is required is;

- 1.83m

- 1.82m

- 1.28m

- 1.38m

- How are escape slides inflated?

- From the bleed air system

- Self contained gas bottle

- Hand pumped by cabin crew

- Using the oral inflation adaptor

- The minimum number of fire extinguishers to be carried in the passenger cabin of an aircraft with 31-60 seats is;

- 3

- 1

- 2

- 4

- The correct type of extinguishant to use on magnesium fires would be;

- CO2

- Freon

- Helium

- Sand

- The correct extinguisher to use on a brake fire would be;

- Foam

- Dry powder

- CO2

- Water

- If an aircraft has a maximum seating configuration of less than 200 but more than 9, a crash axe(or crowbar) must be carried;

- One on the flight deck only

- One on the flight deck and one in the passenger cabin

- Two on the flight deck and one in the forward cargo hold

- One on the flight deck and two in the passenger cabin

- An aircraft is certified to carry a maximum of 240 passengers.  It is configured to carry 200 and has 180 passengers on board.  What is the minimum number of drop down oxygen masks that must be provided?

- 180

- 200

- 220

- 240

- The passenger oxygen drop down oxygen stowage doors are released;

- By a lanyard operated by a barometric capsule

- Mechanically

- Electrically for chemical oxygen generators and pneumatically for gaseous systems

- Manually by the cabin crew

- In a centrifugal compressor;

- The air enters the eye tangentially and leaves the periphery axially

- The air enters the periphery axially and leaves the eye tangentially

- The air enters the eye radially and leaves the tip tangentially

- The air enters the impeller axially at the eye and leaves at the periphery tangentially

- What happens to the pressure, temperature and velocity of the air in the diffuser of a centrifugal compressor?

- Velocity increases, pressure and temperature decrease

- Velocity decreases, pressure and temperature increase

- Velocity, pressure and temperature increase

- Velocity, pressure and temperature decrease

- The type of smoke detector system fitted to aircraft is;

- Optical and ionisation

- Chemical

- Electrical

- Magnetic

- The flight deck warning of an engine fire is;

- Warning bell

- Gear warning

- Warning light and warning bell

- Warning light

- Hydraulic reservoirs are pressurised by;

- Ram air in flight only

- Separate helium gas system

- Air from the air conditioning system

- Bleed air from gas turbine engine

- The purpose of a hydraulic fuse is;

- To allow the parking brake to remain ON overnight, if required

- To allow a reduced pressure to the wheel brake system to avoid locking the wheels

- To prevent over-pressurising the reservoir as altitude increases

- To prevent loss of system fluid if the pipeline to a brake unit should rupture

- A shuttle valve will;

- Allow the accumulator to be emptied after engine shut down

- Reduce pump loading when normal system pressure is achieved

- Automatically switch to the most appropriate source of hydraulic supply

- Operate on a rising pressure, higher than the Full Flow Relief Valve

- With regard to an air cycle type ECS pack, where is the water separator fitted?

- After the humidifier

- Before the CAU compressor

- Between the compressor and the turbine

- After the CAU turbine

- In the event that an emergency descent causes the cabin pressure to decrease below ambient pressure;

- The outward relief valve will open

- The outflow valve will close

- The inward relief valve will open

- The safety valve will close

- The purpose of a ditching control valve is;

- To close the outflow valves

- To open the outflow valves

- To allow rapid depressurisation

- To dump the toilet water after landing

- In a bleed air anti-icing system the areas that are heated are;

- The whole of the wing

- Wing leading edge slats and flaps

- Wing leading edges and slats

- Trailing edge flaps

- On a piston engine aircraft the most likely method of de-icing the wings is;

- Fluid

- Pneumatic boots

- Electrical heater mats

- Hot air from the engines

- If an aircraft maximum operating altitude is limited by cabin pressure, this limit is due to;

- The maximum positive pressure differential at maximum operating ceiling

- The maximum positive pressure differential at maximum cabin altitude

- The maximum number of pressurisation cycles

- The maximum zero fuel mass at maximum pressure altitude

- Regarding a Safe Life structure;

- Will only fail after a known number of operations, or hours of use

- Should not fail until a predicted number of fatigue cycles has been achieved

- Has a programmed inspection cycle to detect and rectify faults

- Is changed before its predicted life is reached

- 1 and 2 apply

- 1 and 3 apply

- 1, 2 and 4 apply

- All apply

- The properties of Duralumin are;

- Aluminium/copper base

- Aluminium/magnesium base

- Hard to weld

- Easy to weld

- Good thermal conductivity

- Poor resistance to air corrosion

- 1, 3, 5

- 2, 3, 5

- 1, 2, 3

- 4, 5, 6

- An undercarriage leg is considered to be locked when;

- It is down

- The amber light is on

- Mechanically locked by an over-centre mechanism

- The actuating cylinder is at the end of its travel

- An under-inflated tyre on a dry runway;

- Increases wear on the shoulder

- Increases wear on the crown

- Increases viscous aquaplaning speed

- Will cause the tyre temperature to decrease

- Kreuger flaps are positioned;

- Towards the wing tip

- At the wing inner leading edge

- Along the whole leading edge

- At the wing trailing edge

- What are flaperons?

- Combined spoiler and flap

- Combined elevators and flaps

- Combined ailerons and elevators

- Combined flap and ailerons

- What is the purpose of inboard ailerons?

- To reduce wing bending at high speed

- To reduce wing twisting at low speed

- To reduce wing bending at low speed

- To reduce wing twisting at high speed

- What is the purpose of trim tabs?

- To reduce stick forces during manoeuvres

- To reduce stick holding forces to zero

- To increase control effectiveness

- To reduce control effectiveness

- Smoke hoods protect;

- Full face, and provide a continuous flow of oxygen

- Mouth and nose, and provide a continuous flow of oxygen

- Full face, and provide oxygen on demand

- Mouth and nose, and provide oxygen on demand

- Oxygen supplied to the flight deck is;

- Gaseous, diluted with ambient air if required

- Chemically generated and diluted with cabin air if required

- Gaseous, diluted with cabin air if required

- Chemically generated, diluted with ambient air if required

- If during pressurised flight the outflow valve closes fully (due to a fault in the controller) the;

- Skin will be overstressed and could rupture

- Safety valve opens when the differential pressure reaches structural maximum differential

- The inward relief valve will open to prevent excessive negative pressure

- ECS packs are automatically closed down

- In a fan jet engine the bypass ratio is;

- Internal mass airflow divided by the external mass airflow

- External mass airflow divided by the internal mass airflow

- Internal mass airflow divided by the fuel flow

- Mass fuel flow divided by the mass airflow

- The amber thrust reverser warning light illuminates on the flight deck annunciator when;

- Thrust reverser doors have moved to the reverse thrust position

- Thrust reverser doors have been selected but the doors haven’t moved

- Thrust reverser doors are locked

- Thrust reverser doors are unlocked

- In very cold weather the pilot notices slightly higher than normal oil pressure on start up.  This;

- Indicates that an oil change is required

- Is indicative of a blocked oil filter

- Is acceptable providing it returns to normal as the engine warms up

- Is abnormal but does not require the engine to be shut down

- In a four stroke engine, when the piston is at BDC at the end of the power stroke the position of the valves is;

- Inlet closed, exhaust open

- Inlet open, exhaust open

- Inlet open, exhaust closed

- Inlet closed, exhaust open

- What is the effect on EGT and EPR if a bleed valve is opened?

- Increase, increase

- Decrease, decrease

- Decrease, increase

- Increase, decrease

- Where is torque measured in a turboprop engine?

- Accessory gearbox

- Reduction gearbox

- At the turbine

- At the constant speed unit oil pump

- Propeller blade angle is;

- The angle between the blade chord and the plane of rotation

- The angle between the relative airflow and the chord line

- Dependent upon RPM and TAS

- The difference between effective pitch and geometric pitch

- Why is a propeller blade twisted?

- To reduce the thrust at the root of the blade

- To prevent the blade from fully feathering

- To reduce tip speed

- To even out the thrust force along the length of the blade

- For calculating resistances in parallel the formula is;

a)

b)

c)

d)

- When a fuse operates it is …………….. and when a circuit breaker operates it is …………….. ;

- High current, low current

- Low current, high current

- Non re-settable, re-settable

- Re-settable, non re-settable

- A hot busbar is one that;

- Supplies galley power

- Is permanently connected to the battery

- Carries all the non-essential loads

- Is connected to the battery in an emergency

- In an AC distribution system what is the purpose of the GCB?

- Maintains constant frequency

- Connects the load busbar to the synchronising busbar

- Control generator field excitation

- Connects a generator to its load busbar

- In an aircraft which uses DC as the primary source of power, AC for the instruments may be obtained from;

- CSDU

- Rectifier

- Inverter

- TRU

- Persistent over-excitation of one generator will cause;

- The GCB and BTB to trip

- The BTB and GFR to trip

- The GCB and GFR to trip

- The GCB and SSB to trip

- When a battery is nearly discharged, does the;

- Voltage decrease

- Voltage and current decrease

- Current increase because the voltage has dropped

- Electrolyte boil

- The state of charge of a battery on an aircraft with a voltmeter would be checked;

- On load

- Off load

- With the battery negative terminal disconnected

- By monitoring the electrolyte resistance

- In a paralleled AC distribution system what regulates the real load?

- Torque from the CSDU

- Field excitation from the voltage regulator

- Synchronising circuits in the BTB

- A potentiometer on the Flight Engineers panel

- What is the correct sequence of events during the start cycle of a gas turbine engine?

- Fuel & ignition on, start selected, light up, self sustaining speed, starter circuit cancelled

- Start selected, fuel & ignition on, light up, starter circuit cancelled, self sustaining speed

- Start selected, fuel & ignition on, light up, self sustaining speed, starter circuit cancelled

- Fuel & ignition on, start selected, self sustaining speed, starter circuit cancelled, light up

AGK REVISION WORKSHEET 1

NAME ……………………….. COURSE …………………..

MARKING GUIDE

|  | A | B | C | D |  |  | A | B | C | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 |  |  |  | X |  | 38 |  |  | X |  |
| 2 | X |  |  |  |  | 39 |  |  |  | X |
| 3 |  |  | X |  |  | 40 |  |  | X |  |
| 4 |  | X |  |  |  | 41 | X |  |  |  |
| 5 | X |  |  |  |  | 42 |  |  | X |  |
| 6 |  | X |  |  |  | 43 |  | X |  |  |
| 7 |  |  |  | X |  | 44 |  | X |  |  |
| 8 |  |  | X |  |  | 45 |  |  | X |  |
| 9 |  | X |  |  |  | 46 | X |  |  |  |
| 10 |  |  |  | X |  | 47 |  |  | X |  |
| 11 |  |  | X |  |  | 48 | X |  |  |  |
| 12 | X |  |  |  |  | 49 |  | X |  |  |
| 13 |  | X |  |  |  | 50 |  |  |  | X |
| 14 | X |  |  |  |  | 51 |  |  |  | X |
| 15 |  |  |  | X |  | 52 |  | X |  |  |
| 16 |  |  | X |  |  | 53 | X |  |  |  |
| 17 |  | X |  |  |  | 54 |  |  | X |  |
| 18 | X |  |  |  |  | 55 |  | X |  |  |
| 19 |  |  |  | X |  | 56 |  | X |  |  |
| 20 |  | X |  |  |  | 57 |  |  |  | X |
| 21 |  |  | X |  |  | 58 |  |  | X |  |
| 22 | X |  |  |  |  | 59 |  |  |  | X |
| 23 |  |  |  | X |  | 60 |  |  |  | X |
| 24 | X |  |  |  |  | 61 |  | X |  |  |
| 25 |  | X |  |  |  | 62 | X |  |  |  |
| 26 |  |  | X |  |  | 63 |  |  |  | X |
| 27 |  |  |  | X |  | 64 |  |  |  | X |
| 28 |  | X |  |  |  | 65 |  |  | X |  |
| 29 | X |  |  |  |  | 66 |  | X |  |  |
| 30 |  |  | X |  |  | 67 |  |  |  | X |
| 31 |  |  | X |  |  | 68 |  |  | X |  |
| 32 |  |  |  | X |  | 69 |  |  | X |  |
| 33 |  | X |  |  |  | 70 |  | X |  |  |
| 34 | X |  |  |  |  | 71 | X |  |  |  |
| 35 |  |  | X |  |  | 72 | X |  |  |  |
| 36 |  |  |  | X |  | 73 |  |  | X |  |
| 37 |  |  |  | X |  | 74 |  |  |  |  |